## Slide 1: LAB-03 Reactive Autonomy
Tanmay Vilas Samak
Ph.D. Candidate
ARMLab, CU-ICAR
Email: tsamak@clemson.edu
Chinmay Vilas Samak
Ph.D. Candidate
ARMLab, CU-ICAR
Email: csamak@clemson.edu

## Slide 2: Lab Outline and Expected Outcomes
Emergency braking
  Formulation A: Single measurement
  Formulation B: Multiple measurements
Wall following
  Formulation A: Follow just one wall
  Formulation B: Follow both the walls
Gap following
  Formulation A: Naïve gap follower
  Formulation B: Disparity extender
GOAL: Perception-enhanced vehicle control

## Slide 3
Emergency Braking

## Slide 4: Formulation A: Single Measurement
Consider a frontal laser beam
The laser beam measures distance w.r.t. LIDAR
The LIDAR is offset from the front bumper by a distance
Hence, the distance to collision is
Let a safe DTC threshold be (e.g., 3 wheelbase)
Emergency braking behavior requires:
Zero steering angle is enforced:
Instead of hard-braking, you can implement a controller to reduce the velocity proportional to the DTC for smoother braking.

## Slide 5: Formulation B: Multiple Measurements
Small issue: Using a single measurement can be suboptimal. A spurious return due to any reason (noise, dust, a reflection) can become the new minimum and seem like an obstacle (a.k.a. the “ghost obstacle” problem in autonomous racing). A vehicle traveling at high speeds may not have enough time to recover and may crash!
Proposed solution: We can consider multiple range measurements across a small sector on the front. The frontal distance can be then computed as the mean of these readings, which is more stable/reliable.
Let a safe DTC threshold be (e.g., 3 wheelbase)
Emergency braking behavior requires:
Zero steering angle is enforced:

## Slide 6: Emergency Braking Demo
Reference Code
Secondary Objective:
Performance
Assessment:
Distance to collision 1 m
Primary Objective:
Safety
Assessment:
Collision count 0

## Slide 7
Wall Following

## Slide 8: Formulation A: Follow Just One Wall
Let the distance to the right wall at the current time be
Let the vehicle be oriented at an angle w.r.t. right wall
Consider two laser beams:
exactly to the right of the vehicle
any arbitrary angle w.r.t. beam
Using trigonometry, we can express
We can then express
Cross-track error is the difference between and a reference
The lateral controller then acts on this error:

## Slide 9: Formulation A: Follow Just One Wall
Small issue: The vehicle will be traveling at a high speeds and will have a non-instantaneous response to whatever speed and steering commands are computed. If we simply use the current distance to the wall, the vehicle might end up turning too late and may crash!
Proposed solution: We can account for this delay and project the vehicle ahead by a certain lookahead distance (let's call it ).
We can express projected distance to the wall
Cross-track error is now the difference between and
The lateral controller then acts on this error:
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on steering.

## Slide 10: Formulation B: Follow Both the Walls
Consider two laser beams:
exactly to the left of the vehicle
exactly to the right of the vehicle
Let the distance to the left wall at the current time be
Let the distance to the right wall at the current time be
Cross-track error is the difference between and
The lateral controller then acts on this error:
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on steering.

## Slide 11: Formulation B: Follow Both the Walls
Small issue: Using a single measurement can be suboptimal. A spurious return due to any reason (noise, dust, a reflection) can destabilize the controller and compromise its behavior. Vehicle traveling at high speed may not have enough time to recover and may crash!
Proposed solution: We can consider multiple range measurements across a small sector on either sides. The left and right distances can be then computed as the mean of these readings, which is more stable/reliable.
Cross-track error is the difference between and
The lateral controller then acts on this error:
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on steering.

## Slide 12: Wall Following Demo
Reference Code
Secondary Objective:
Performance
Assessment:
Minimize lap time
Primary Objective:
Safety
Assessment:
Collision count 0

## Slide 13
Gap Following

## Slide 14: Formulation A: Naïve Gap Follower
Step 1: Register LIDAR range array
ranges = […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Find the angle corresponding to the largest range value
Step 3: Drive in that direction
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on frontal LIDAR measurement(s).
Small issue: The LIDAR rays used to identify the furthest visible point are practically zero-width, but the vehicle has a non-zero width. If the vehicle simply drives towards this point, it might collide with the track bounds!

## Slide 15: Formulation A: Naïve Gap Follower
Step 1: Register LIDAR range array
ranges = […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Find the angle corresponding to the largest range value
Step 3: Drive in that direction
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on frontal LIDAR measurement(s).
Small issue: The LIDAR rays used to identify the furthest visible point are practically zero-width, but the vehicle has a non-zero width. If the vehicle simply drives towards this point, it might collide with the track bounds!

## Slide 16: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.

## Slide 17: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]

## Slide 18: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]

## Slide 19: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]

## Slide 20: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]
Step 4: Extend the disparity […, 2.1, 2.2, 2.2, 2.2, …]
 | Width of the vehicle footprint Safety margin Range at the closer index

## Slide 21: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]
Step 4: Extend the disparity […, 2.1, 2.2, 2.2, 2.2, …]
Repeat this process for every disparity but never overwrite closer ranges with farther ones.
 | Width of the vehicle footprint Safety margin Range at the closer index

## Slide 22: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]
Step 4: Extend the disparity […, 2.1, 2.2, 2.2, 2.2, …]
Step 5: Target the farthest reachable point

## Slide 23: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]
Step 4: Extend the disparity […, 2.1, 2.2, 2.2, 2.2, …]
Step 5: Target the farthest reachable point
You can smoothen the steering rate by weighing it against the previous steering command:

## Slide 24: Formulation B: Disparity Extender
Proposed solution: We can account for the vehicle footprint by extending the disparity of LIDAR measurements.
Step 1: Register LIDAR range array […, 2.1, 2.2, 4.8, 4.2, …]
Step 2: Filter frontal measurements […, 2.1, 2.2, 4.8, 4.2, …]
Step 3: Find a disparity […, 2.1, 2.2, 4.8, 4.2, …]
Step 4: Extend the disparity […, 2.1, 2.2, 2.2, 2.2, …]
Step 5: Target the farthest reachable point
You can smoothen the steering rate by weighing it against the previous steering command:
The longitudinal controller can track a velocity setpoint by controlling the throttle: , or adapt the velocity based on frontal LIDAR measurement(s).

## Slide 25: Gap Following Demo
Secondary Objective:
Performance
Assessment:
Minimize lap time
Primary Objective:
Safety
Assessment:
Collision count 0
Reference Code

## Slide 26
Open to questions and discussion…
Thank You!